husseinnasser
The IP building blocks
1.2.3.4
Understanding the IP Protocol

---
IP Address
IP Address
- Layer 3 property
- Can be set automatically or statically
- Network and Host portion
- 4 bytes in IPv4 - 32 bits

---
Network vs Host
Network vs Host
- a.b.c.d/x (a.b.c.d are integers) x is the network bits and remains are host
- Example 192.168.254.0/24
- The first 24 bits (3 bytes) are network the rest 8 are for host
- This means we can have 2^24 (16777216) networks and each network has 2^8 (255) hosts
- Also called a subnet

---
Subnet Mask
Subnet Mask
- 192.168.254.0/24 is also called a subnet
- The subnet has a mask 255.255.255.0
- Subnet mask is used to determine whether an IP is in the same subnet

---
Default Gateway
Default Gateway
- Most networks consists of hosts and a Default Gateway
- Host A can talk to B directly if both are in the same subnet
- Otherwise A sends it to someone who might know, the gateway
- The Gateway has an IP Address and each host should know its gateway

---
E.g. Host 192.168.1.3 wants to talk to 192.168.1.2
E.g. Host 192.168.1.3 wants to talk to 192.168.1.2
- 192.168.1.3 applies subnet mask to itself and the destination IP 192.168.1.2
- 255.255.255.0 &
  192.168.1.3 =
  192.168.1.0
- 255.255.255.0 &
  192.168.1.2 =
  192.168.1.0
- Same subnet ! no need to route
192.168.2.3
192.168.1.3
192.168.2.2
192.168.1.2
192.168.1.1
192.168.2.1
192.168.1.0/24
192.168.2.0/24

---
E.g. Host 192.168.1.3 wants to talk to 192.168.2.2
E.g. Host 192.168.1.3 wants to talk to 192.168.2.2
- 192.168.1.3 applies subnet mask to itself and the destination IP 192.168.2.2
- 255.255.255.0 &
  192.168.1.3 =
  192.168.1.0
- 255.255.255.0 &
  192.168.2.2 =
  192.168.2.0
- Not the subnet ! The packet is sent to the Default Gateway 192.168.1.100
192.168.2.100
192.168.2.3
192.168.1.3
192.168.1.100
192.168.2.2
192.168.1.2
192.168.1.1
192.168.2.1
192.168.1.0/24
192.168.2.0/24

---
Summary
Summary
- IP Address
- Network vs Host
- Subnet and subnet mask
- Default Gateway

---
The IP Packet
Anatomy of the IP Packet

---
IP Packet
IP Packet
- The IP Packet has headers and data sections
- IP Packet header is 20 bytes (can go up to 60 bytes if options are enabled)
- Data section can go up to 65536

---
IP Packet to the Backend Engineer
IP Packet to the Backend Engineer
Source IP Address
        Data
Destination IP Address

---
Actual IP Packet
Actual IP Packet
Offsets		0					1					2					3
		0	1	2	3	4	5	6	7	8	9	10	11	12	13	14	15	16	17	18	19	20	21	22	23	24	25	26	27	28	29	30	31
0	0
4	32
8	64
12	96
16	128
20	160	Options (if IHL > 5)
⋮	⋮
56	448
Data
https://datatracker.ietf.org/doc/html/rfc791
https://en.wikipedia.org/wiki/IPv4

---
Version - The Protocol version
Version - The Protocol version
Offsets		0					1					2					3
		0	1	2	3	4	5	6	7	8	9	10	11	12	13	14	15	16	17	18	19	20	21	22	23	24	25	26	27	28	29	30	31
0	0
4	32
8	64
12	96
16	128
20	160	Options (if IHL > 5)
⋮	⋮
56	448
Data

---
Internet Header Length - Defines the Options length
Internet Header Length - Defines the Options length
Offsets		0					1					2					3
		0	1	2	3	4	5	6	7	8	9	10	11	12	13	14	15	16	17	18	19	20	21	22	23	24	25	26	27	28	29	30	31
0	0
4	32
8	64
12	96
16	128
20	160	Options (if IHL > 5)
⋮	⋮
56	448
Data

---
Total Length - 16 bit Data + header
Total Length - 16 bit Data + header
Offsets		0					1					2					3
		0	1	2	3	4	5	6	7	8	9	10	11	12	13	14	15	16	17	18	19	20	21	22	23	24	25	26	27	28	29	30	31
0	0
4	32
8	64
12	96
16	128
20	160	Options (if IHL > 5)
⋮	⋮
56	448
Data

---
Fragmentation - Jumbo packets
Fragmentation - Jumbo packets
Offsets		0					1					2					3
		0	1	2	3	4	5	6	7	8	9	10	11	12	13	14	15	16	17	18	19	20	21	22	23	24	25	26	27	28	29	30	31
0	0
4	32
8	64
12	96
16	128
20	160	Options (if IHL > 5)
⋮	⋮
56	448
Data

---
Time To Live - How many hops can this packet survive?
Time To Live - How many hops can this packet survive?
Offsets		0					1					2					3
		0	1	2	3	4	5	6	7	8	9	10	11	12	13	14	15	16	17	18	19	20	21	22	23	24	25	26	27	28	29	30	31
0	0
4	32
8	64
12	96
16	128
20	160	Options (if IHL > 5)
⋮	⋮
56	448
Data

---
Protocol - What protocol is inside the data section?
Protocol - What protocol is inside the data section?
Offsets		0					1					2					3
		0	1	2	3	4	5	6	7	8	9	10	11	12	13	14	15	16	17	18	19	20	21	22	23	24	25	26	27	28	29	30	31
0	0
4	32
8	64
12	96
16	128
20	160	Options (if IHL > 5)
⋮	⋮
56	448
Data

---
Source and Destination IP
Source and Destination IP
Offsets		0					1					2					3
		0	1	2	3	4	5	6	7	8	9	10	11	12	13	14	15	16	17	18	19	20	21	22	23	24	25	26	27	28	29	30	31
0	0
4	32
8	64
12	96
16	128
20	160	Options (if IHL > 5)
⋮	⋮
56	448
Data

---
Explicit Congestion Notification
Explicit Congestion Notification
Offsets		0					1					2					3
		0	1	2	3	4	5	6	7	8	9	10	11	12	13	14	15	16	17	18	19	20	21	22	23	24	25	26	27	28	29	30	31
0	0
4	32
8	64
12	96
16	128
20	160	Options (if IHL > 5)
⋮	⋮
56	448
Data
[Speaker Notes: ECN is an IP and TCP option, if the router experienced congestion,dont’ drop the packet instead set this bit so the TCP layer can half the congestion window and slow down.]

---
Summary
Summary
- The IP Packet has headers and data sections
- IP Packet header is 20 bytes (can go up to 60 bytes if options are enabled)
- Data section can go up to 65536
- Packets need to get fragmented if it doesn’t fit in a frame

---
ICMP
Internet Control Message Protocol

---
ICMP
ICMP
- Stands for Internet Control Message Protocol
- Designed for informational messages
  - Host unreachable, port unreachable, fragmentation needed
  - Packet expired (infinite loop in routers)
- Uses IP directly
- PING and traceroute use it
- Doesn’t require listeners or ports to be opened

---
ICMP header
ICMP header
Offsets		0					1					2					3
		0	1	2	3	4	5	6	7	8	9	10	11	12	13	14	15	16	17	18	19	20	21	22	23	24	25	26	27	28	29	30	31
0	0
4	32
https://en.wikipedia.org/wiki/Internet_Control_Message_Protocol
https://datatracker.ietf.org/doc/html/rfc792

---
ICMP
ICMP
- Some firewalls block ICMP for security reasons
- That is why PING might not work in those cases
- Disabling ICMP also can cause real damage with connection establishment
  - Fragmentation needed
- PING demo

---
Ping
Ping
192.168.10.100
192.168.5.100
192.168.10.3
192.168.1.3
192.168.10.3
192.168.1.3
TTL96 ICMP echo request
192.168.1.100
192.168.10.3
192.168.1.3
TTL100 ICMP echo request
192.168.1.3
192.168.10.3
TTL100 ICMP echo reply
192.168.1.3
192.168.10.3
TTL96 ICMP echo reply
192.168.3.100

---
Ping - unreachable
Ping - unreachable
192.168.10.100
192.168.5.100
192.168.10.3
192.168.10.3
192.168.1.3
TTL0 ICMP echo request
192.168.1.3
192.168.5.100
TTL100 ICMP dest unreachable
192.168.1.3
192.168.1.100
192.168.10.3
192.168.1.3
TTL3 ICMP echo request
192.168.1.3
192.168.5.100
TTL96 ICMP echo reply
192.168.3.100

---
TraceRoute
TraceRoute
- Can you identify the entire path your IP Packet takes?
- Clever use of TTL
- Increment TTL slowly and you will get the router IP address for each hop
- Doesn’t always work as path changes and ICMP might be blocked

---
Traceroute
Traceroute
192.168.10.100
192.168.5.100
192.168.10.3
192.168.1.3
192.168.1.100
192.168.1.3
192.168.1.100
ICMP dest unreach.
192.168.10.3
192.168.1.3
TTL2 ICMP echo request
192.168.3.100
192.168.1.3
192.168.3.100
ICMP dest unreach.
192.168.10.3
192.168.1.3
TTL3 ICMP echo request
192.168.1.3
192.168.5.100
ICMP dest unreach.
192.168.10.3
192.168.1.3
TTL4 ICMP echo request
192.168.1.3
192.168.10.100
ICMP dest unreach
192.168.10.3
192.168.1.3
TTL5 ICMP echo request
192.168.1.3
192.168.10.3
ICMP Echo reply
192.168.1.3
TTL1 ICMP echo request
192.168.10.3

---
Summary
Summary
- ICMP is an IP level protocol used for information messages
- Critical to know if the host is available or port is opened
- Used for PING and TraceRoute
- Can be blocked which can cause problems

---
ARP
Address Resolution Protocol

---
Why ARP?
Why ARP?
- We need the MAC address to send frames (layer 2)
- Most of the time we know the IP address but not the MAC
- ARP Table is cached IP->Mac mapping

---
Network Frame
Network Frame
aa:bc:32:7f:c0:07
10.0.0.2
2312
GET /
8080
10.0.0.3
bb:ab:dd:11:22:33
aa
2
GET /
3
bb
IP : 10.0.0.2
MAC: aa:bc:32:7f:c0:07
IP : 10.0.0.3
MAC: bb:ab:dd:11:22:33
Port: 8080

---
IP 10.0.0.2 (2) wants to connect to IP 10.0.0.5 (5)
Host 2 checks if host 5 is within its subnet, it is.
Host 2 needs the MAC address of host 5
Host 2 checks its ARP tables and its not there
EXIP : 122.1.2.4
IP : 10.0.0.1 (1)
MAC: ff
aa
2
GET /
5
??
ip	mc
2	aa
ip	mc
3	bb
ip	mc
4	cc
ip	mc
5	dd
IP : 2
GW : 1
MAC: aa
IP : 3
GW : 1
MAC: bb
IP : 4
GW : 1
MAC: cc
IP : 5
GW : 1
MAC: dd

---
Host 2 sends an ARP request broadcast to all machines in its network
Who has IP address 10.0.0.5?
Host 5 replies with dd
Host 2 updates its ARP Table
EXIP : 122.1.2.4
IP : 10.0.0.1 (1)
MAC: ff
aa
2
GET /
5
dd
ip	mc
2	aa
5	dd
ip	mc
3	bb
ip	mc
4	cc
ip	mc
5	dd
IP : 2
GW : 1
MAC: aa
IP : 3
GW : 1
MAC: bb
IP : 4
GW : 1
MAC: cc
IP : 5
GW : 1
MAC: dd

---
IP 10.0.0.2 (2) wants to connect to IP 1.2.3.4 (x)
Host 2 checks if 1.2.3.4 is within its subnet, it is NOT!
Host 2 needs to talk to its gatway
Host 2 needs the MAC address of the gateway
EXIP : 122.1.2.4
IP : 10.0.0.1 (1)
MAC: ff
1.2.3.4 (x)
aa
2
GET /
x
??
ip	mc
2	aa
5	dd
ip	mc
3	bb
ip	mc
4	cc
ip	mc
5	dd
IP : 2
GW : 1
MAC: aa
IP : 3
GW : 1
MAC: bb
IP : 4
GW : 1
MAC: cc
IP : 5
GW : 1
MAC: dd

---
Host 2 checks its local ARP table, 10.0.0.1 is not it in
Host 2 sends an ARP request to everybody in the network
Who has 10.0.0.1? (A DANGEROUS QUESTION)
Gateway reply with ff
NAT than kicks in.
EXIP : 122.1.2.4
IP : 10.0.0.1 (1)
MAC: ff
1.2.3.4
aa
2
GET /
x
ff
ip	mc
2	aa
5	dd
1	ff
ip	mc
3	bb
ip	mc
4	cc
ip	mc
5	dd
IP : 2
GW : 1
MAC: aa
IP : 3
GW : 1
MAC: bb
IP : 4
GW : 1
MAC: cc
IP : 5
GW : 1
MAC: dd

---
Summary
Summary
- ARP stands for Address resolution protocol
- We need MAC address to send frames between machines
- Almost always we have the IP address but not the MAC
- Need a lookup protocol that give us the MAC from IP address
- Attacks can be performed on ARP (ARP poisoning)

---
Routing Example
How IP Packets are routed in Switches and Routers

---
Switch (S)
10.0.0.4
10.0.0.2
Router (R)
10.0.0.5
10.0.0.100
10.0.0.3
192.168.1.1
192.168.1.2
A -> B
D -> X
B -> G
1.2.3.4
Internet
8.8.8.8 (G)
A
D
B
C
X

---
UDP
User Datagram Protocol

---
UDP
UDP
- Stands for User Datagram Protocol
- Layer 4 protocol
- Ability to address processes in a host using ports
- Simple protocol to send and receive data
- Prior communication not required (double edge sword)
- Stateless no knowledge is stored on the host
- 8 byte header Datagram

---
UDP Use cases
UDP Use cases
- Video streaming
- VPN
- DNS
- WebRTC
B
A

---
Multiplexing and demultiplexing
Multiplexing and demultiplexing
- IP target hosts only
- Hosts run many apps each with different requirements
- Ports now identify the “app” or “process”
- Sender multiplexes all its apps into UDP
- Receiver demultiplex UDP datagrams to each app
AppX-port 53
AppY-port 68
AppZ-port 6978
App1-port 5555
App2-port 7712
App3-port 2222
10.0.0.1
10.0.0.2

---
Source and Destination Port
Source and Destination Port
- App1 on 10.0.0.1 sends data to AppX on 10.0.0.2
- Destination Port = 53
- AppX responds back to App1
- We need Source Port so we know how to send back data
- Source Port = 5555
10.0.0.1
5555
53
10.0.0.2
AppX-port 53
AppY-port 68
AppZ-port 6978
App1-port 5555
App2-port 7712
App3-port 2222
10.0.0.2
53
5555
10.0.0.1
10.0.0.1
10.0.0.2

---
Summary
Summary
- UDP is a simple layer 4 protocol
- Uses ports to address processes
- Stateless

---
UDP Datagram
The anatomy of the UDP datagram

---
UDP Datagram
UDP Datagram
- UDP Header is 8 bytes only (IPv4)
- Datagram slides into an IP packet as “data”
- Port are 16 bit (0 to 65535)

---
UDP Datagram header
UDP Datagram header
Offsets		0					1					2					3
		0	1	2	3	4	5	6	7	8	9	10	11	12	13	14	15	16	17	18	19	20	21	22	23	24	25	26	27	28	29	30	31
0	0	Source port					Destination port
4	32	Length					Checksum
Data
https://www.ietf.org/rfc/rfc768.txt
https://en.wikipedia.org/wiki/User_Datagram_Protocol

---
Source Port and Destination Port
Source Port and Destination Port
Offsets		0					1					2					3
		0	1	2	3	4	5	6	7	8	9	10	11	12	13	14	15	16	17	18	19	20	21	22	23	24	25	26	27	28	29	30	31
0	0	Source port					Destination port
4	32	Length					Checksum
Data

---
Length & Checksum
Length & Checksum
Offsets		0					1					2					3
		0	1	2	3	4	5	6	7	8	9	10	11	12	13	14	15	16	17	18	19	20	21	22	23	24	25	26	27	28	29	30	31
0	0	Source port					Destination port
4	32	Length					Checksum
Data

---
UDP Pros and Cons
The power and drawbacks of UDP

---
UDP Pros
UDP Pros
- Simple protocol
- Header size is small so datagrams are small
- Uses less bandwidth
- Stateless
- Consumes less memory (no state stored in the server/client)
- Low latency - no handshake , order, retransmission or guaranteed delivery

---
UDP Cons
UDP Cons
- No acknowledgement
- No guarantee delivery
- Connection-less - anyone can send data without prior knowledge
- No flow control
- No congestion control
- No ordered packets
- Security - can be easily spoofed

---
TCP
Transmission Control Protocol

---
TCP
TCP
- Stands for Transmission Control Protocol
- Layer 4 protocol
- Ability to address processes in a host using ports
- “Controls” the transmission unlike UDP which is a firehose
- Connection
- Requires handshake
- 20 bytes headers Segment (can go to 60)
- Stateful

---
TCP Use cases
TCP Use cases
- Reliable communication
- Remote shell
- Database connections
- Web communications
- Any bidirectional communication
B
A

---
TCP Connection
TCP Connection
- Connection is a Layer 5 (session)
- Connection is an agreement between client and server
- Must create a connection to send data
- Connection is identified by 4 properties
  - SourceIP-SourcePort
  - DestinationIP-DestinationPort

---
TCP Connection
TCP Connection
- Can’t send data outside of a connection
- Sometimes called socket or file descriptor
- Requires a 3-way TCP handshake
- Segments are sequenced and ordered
- Segments are acknowledged
- Lost segments are retransmitted

---
Multiplexing and demultiplexing
Multiplexing and demultiplexing
- IP target hosts only
- Hosts run many apps each with different requirements
- Ports now identify the “app” or “process”
- Sender multiplexes all its apps into TCP connections
- Receiver demultiplex TCP segments to each app based on connection pairs
AppX-port 53
AppY-port 68
AppZ-port 6978
App1-port 5555
App2-port 7712
App3-port 2222
10.0.0.1
10.0.0.2

---
Connection Establishment
Connection Establishment
- App1 on 10.0.0.1 want to send data to AppX on 10.0.0.2
- App1 sends SYN to AppX to synchronous sequence numbers
- AppX sends SYN/ACK to synchronous its sequence number
- App1 ACKs AppX SYN.
- Three way handshake
5555
SYN
10.0.0.2
10.0.0.1
22
AppX-port 22
AppY-port 443
AppZ-port 80
App1-port 5555
App2-port 7712
App3-port 2222
22
SYN/ACK
10.0.0.1
10.0.0.2
5555
10.0.0.1:5555:10.0.0.2:22
10.0.0.1
10.0.0.2
10.0.0.1:5555:10.0.0.2:22
5555
ACK
10.0.0.2
10.0.0.1
22
File descriptor
File descriptor

---
Sending data
Sending data
- App1 sends data to AppX
- App1 encapsulate the data in a segment and send it
- AppX acknowledges the segment
- Hint: Can App1 send new segment before ack of old segment arrives?
5555
ls
10.0.0.2
10.0.0.1
22
AppX-port 22
AppY-port 443
AppZ-port 80
App1-port 5555
App2-port 7712
App3-port 2222
22
ACK
10.0.0.1
10.0.0.2
5555
10.0.0.1:5555:10.0.0.2:22
10.0.0.1
10.0.0.2
10.0.0.1:5555:10.0.0.2:22
File descriptor
File descriptor

---
Acknowledgment
Acknowledgment
- App1 sends segment 1,2 and 3 to AppX
- AppX acknowledge all of them with a single ACK 3
5555
seq1
10.0.0.2
10.0.0.1
22
AppX-port 22
AppY-port 443
AppZ-port 80
App1-port 5555
App2-port 7712
App3-port 2222
5555
seq2
10.0.0.2
10.0.0.1
22
5555
seq3
10.0.0.2
10.0.0.1
22
10.0.0.1
10.0.0.1:5555:10.0.0.2:22
10.0.0.2
10.0.0.1:5555:10.0.0.2:22
File descriptor
File descriptor
22
ACK3
10.0.0.1
10.0.0.2
5555

---
Lost data
Lost data
- App1 sends segment 1,2 and 3 to AppX
- Seg 3 is lost, AppX acknowledge 3
- App1 resend Seq 3
5555
seq1
10.0.0.2
10.0.0.1
22
AppX-port 22
AppY-port 443
AppZ-port 80
App1-port 5555
App2-port 7712
App3-port 2222
5555
seq2
10.0.0.2
10.0.0.1
22
5555
seq3
10.0.0.2
10.0.0.1
22
10.0.0.1
10.0.0.1:5555:10.0.0.2:22
10.0.0.2
10.0.0.1:5555:10.0.0.2:22
File descriptor
22
ACK2
10.0.0.1
10.0.0.2
5555
File descriptor
5555
seq3
10.0.0.2
10.0.0.1
22
22
ACK3
10.0.0.1
10.0.0.2
5555

---
Closing Connection
Closing Connection
- App1 wants to close the connection
- App1 sends FIN, AppX ACK
- AppX sends FIN, App1 ACK
- Four way handshake
5555
FIN
10.0.0.2
10.0.0.1
22
AppX-port 22
AppY-port 443
AppZ-port 80
App1-port 5555
App2-port 7712
App3-port 2222
22
ACK
10.0.0.1
10.0.0.2
5555
10.0.0.1:5555:10.0.0.2:22
10.0.0.1
10.0.0.2
10.0.0.1:5555:10.0.0.2:22
22
FIN
10.0.0.1
10.0.0.2
5555
File descriptor
File descriptor
5555
ACK
10.0.0.2
10.0.0.1
22

---
Summary
Summary
- Stands for Transmission Control Protocol
- Layer 4 protocol
- “Controls” the transmission unlike UDP which is a firehose
- Introduces Connection concept
- Retransmission, acknowledgement, guaranteed delivery
- Stateful, connection has a state

---
TCP Segment
The anatomy of the TCP Segment

---
TCP Segment
TCP Segment
- TCP segment Header is 20 bytes and can go up to 60 bytes
- TCP segments slides into an IP packet as “data”
- Port are 16 bit (0 to 65535)
- Sequences, Acknowledgment, flow control and more

---
TCP Segment
TCP Segment
Offsets		0					1					2					3
Octet		7	6	5	4	3	2	1	0	7	6	5	4	3	2	1	0	7	6	5	4	3	2	1	0	7	6	5	4	3	2	1	0
0	0	Source port					Destination port
4	32	Sequence number
8	64	Acknowledgment number (if ACK set)
12	96	Data offset				Reserved / 0 0 0			NS	CWR	ECE	URG	ACK	PSH	RST	SYN	FIN	Window Size
16	128	Checksum					Urgent pointer (if URG set)
20	160	Options (if data offset > 5. Padded at the end with "0" bits if necessary.)
⋮	⋮
60	480
https://en.wikipedia.org/wiki/Transmission_Control_Protocol
https://datatracker.ietf.org/doc/html/rfc793

---
Ports
Ports
Offsets		0					1					2					3
Octet		7	6	5	4	3	2	1	0	7	6	5	4	3	2	1	0	7	6	5	4	3	2	1	0	7	6	5	4	3	2	1	0
0	0	Source port					Destination port
4	32	Sequence number
8	64	Acknowledgment number (if ACK set)
12	96	Data offset				Reserved / 0 0 0			NS	CWR	ECE	URG	ACK	PSH	RST	SYN	FIN	Window Size
16	128	Checksum					Urgent pointer (if URG set)
20	160	Options (if data offset > 5. Padded at the end with "0" bits if necessary.)
⋮	⋮
60	480

---
Sequences and ACKs
Sequences and ACKs
Offsets		0					1					2					3
Octet		7	6	5	4	3	2	1	0	7	6	5	4	3	2	1	0	7	6	5	4	3	2	1	0	7	6	5	4	3	2	1	0
0	0	Source port					Destination port
4	32	Sequence number
8	64	Acknowledgment number (if ACK set)
12	96	Data offset				Reserved / 0 0 0			NS	CWR	ECE	URG	ACK	PSH	RST	SYN	FIN	Window Size
16	128	Checksum					Urgent pointer (if URG set)
20	160	Options (if data offset > 5. Padded at the end with "0" bits if necessary.)
⋮	⋮
60	480

---
Flow Control Window Size
Flow Control Window Size
Offsets		0					1					2					3
Octet		7	6	5	4	3	2	1	0	7	6	5	4	3	2	1	0	7	6	5	4	3	2	1	0	7	6	5	4	3	2	1	0
0	0	Source port					Destination port
4	32	Sequence number
8	64	Acknowledgment number (if ACK set)
12	96	Data offset				Reserved / 0 0 0			NS	CWR	ECE	URG	ACK	PSH	RST	SYN	FIN	Window Size
16	128	Checksum					Urgent pointer (if URG set)
20	160	Options (if data offset > 5. Padded at the end with "0" bits if necessary.)
⋮	⋮
60	480

---
9 bit flags
9 bit flags
Offsets		0					1					2					3
Octet		7	6	5	4	3	2	1	0	7	6	5	4	3	2	1	0	7	6	5	4	3	2	1	0	7	6	5	4	3	2	1	0
0	0	Source port					Destination port
4	32	Sequence number
8	64	Acknowledgment number (if ACK set)
12	96	Data offset				Reserved / 0 0 0			NS	CWR	ECE	URG	ACK	PSH	RST	SYN	F I / N	Window Size
16	128	Checksum					Urgent pointer (if URG set)
20	160	Options (if data offset > 5. Padded at the end with "0" bits if necessary.)
⋮	⋮
60	480

---
Maximum Segment Size
Maximum Segment Size
- Segment Size depends the MTU of the network
- Usually 512 bytes can go up to 1460
- Default MTU in the Internet is 1500 (results in MSS 1460)
- Jumbo frames MTU goes to 9000 or more
- MSS can be larger in jumbo frames cases

---
TCP Pros and Cons
The power and drawbacks of TCP

---
TCP Pros
TCP Pros
- Guarantee delivery
- No one can send data without prior knowledge
- Flow Control and Congestion Control
- Ordered Packets no corruption or app level work
- Secure and can’t be easily spoofed

---
TCP Cons
TCP Cons
- Large header overhead compared to UDP
- More bandwidth
- Stateful - consumes memory on server and client
- Considered high latency for certain workloads (Slow start/ congestion/ acks)
- Does too much at a low level (hence QUIC)
  - Single connection to send multiple streams of data (HTTP requests)
  - Stream 1 has nothing to do with Stream 2
  - Both Stream 1 and Stream 2 packets must arrive
- TCP Meltdown
  - Not a good candidate for VPN

---
Overview of Popular Networking Protocols
Overview of Popular Networking Protocols

---
TLS
Transport Layer Security

---
TLS
TLS
- Vanilla HTTP
- HTTPS
- TLS 1.2 Handshake
- Diffie Hellman
- TLS 1.3 Improvements

---
close
HTTP
80
open
close
….
GET /
Headers+ index.html
<html>...

---
close
HTTPS
open
443
….
close
Handshake
Headers+ index.html
<html>...
GET /

---
Why TLS
Why TLS
- We encrypt with symmetric key algorithms
- We need to exchange the symmetric key
- Key exchange uses asymmetric key (PKI)
- Authenticate the server
- Extensions (SNI, preshared, 0RTT)

---
close
RSA Public key
TLS1.2
open
RSA Private key
close
….
Client hello
Server hello (cert)
Change cipher, fin
GET /
Headers+ index.html
<html>...
Change cipher, fin

---
Diffie Hellman
Diffie Hellman
Private x
+
=
Public g,n
Symmetric key
+
Private y

---
Diffie Hellman
Diffie Hellman
+
Public/
Unbreakable
/can be shared
g^x % n
Public/
Unbreakable
/can be shared
g^y % n
+
(g^x % n)^y = g^xy % n
(g^y % n)^x = g^xy % n

---
close
TLS1.3
open
….
close
(g^x % n)^y = g^xy % n
(g^y % n)^x = g^xy % n
GET /
Headers+ index.html
<html>...
server hello/ change cipher/ fin
client hello / key /fin

---
TLS Summary
TLS Summary
- Vanilla HTTP
- HTTPS
- TLS 1.2 Handshake	(two round trips)
- Diffie Hellman
- TLS 1.3 Improvements (one round trip can be zero)